## Slide 1
Integrating Triboelectric Nanogenerators with TiO2-based UV Photodetectors for Self-Powered Sensor Systems

## Slide 2
Dr. Raheleh Mohammadpour
Maedeh Taherkhani

## Slide 3
Applications

## Slide 4
Applications
Imaging systems
Optical Communications
Industrial monitoring
Electronic devices
Scientific research
Cameras, Security, Medical imging
Fiber optic cables, Optical switches
Environmental sensors, Remote sensing
Wearable devices, Smartphones, VR, AR
Spectroscopy, Astronomy, Particle physics

## Slide 5
Introduction

## Slide 6
Triboelectric Nanogenerator
Introduction
A contact induced electrification in which a material becomes electrically charged after it is contacted with a different material through friction.

## Slide 7
Working mechanism of TENGs
Introduction
Two insulators contact each other

## Slide 8
Working mechanism of TENGs
Introduction
+ + + + + + + +
- - - - - - - -
+ + + + + + + +
- - - - - - - -
According to the triboelectrification series, one of the surfaces becomes positively charged while the other becomes negatively charged upon contact.
The charged surfaces, causes charge induction in the electrodes and through the movement of the surfaces, a current will appear in the external circuit.

## Slide 9
Photodetector
Introduction
Photodetection is a technology that converts incident light signal to electrical signal, which has been exploited widely for practical applications, such as light communication, medical, geological, industrial, photoimaging, civil, and so on.

## Slide 10
Introduction
Rutile
Anatase
Brookite

## Slide 11
Introduction
Rutile
Anatase
Brookite
3 eV
3.2 eV
Most stable at high Temp.
More stable in nano sized-particles
Instable

## Slide 12
Low temp. stable crystal
Suitable band gap
Excellent electron mobility
UV absorptivity
High visible light transmittance
Introduction
Anatase

## Slide 13
UV light
Introduction
UV light comprises a segment of the electromagnetic spectrum between 400 and 100 nm, corresponding to photon energies from 3 to 124 eV.
UV-A (400 to 315 nm)
UV-B (315 to 280 nm)
UV-C (280 to 200 nm)  very high energy and destructive
Vacuum UV

## Slide 14
Working mechanism of semiconductor-based PDs
Introduction
Au
Au
e-h
Resistor
R
I

## Slide 15
Working mechanism of semiconductor-based PDs
Introduction
Au
Au
UV
e
e
e
e
h
h
h
h
e
h
e-h
R
I

## Slide 16
Fabrication

## Slide 17
Triboelectric Nanogenerator
Fabrication
Kapton
Al

## Slide 18
Photodetector
Fabrication
Glass
Au
Au
Sputtering
Mask

## Slide 19
Photodetector
Fabrication
Glass
Au
Au
Sputtering
Mask
Doctor Blading
paste
Nanoparticle - Anatase
Size: Around 20 nm

## Slide 20
Photodetector
Fabrication
Glass
Au
Au
FTO (Fluorine doped tin oxide)

## Slide 21
Final Device
Fabrication
Glass
Au
Au
FTO (Fluorine doped tin oxide)
Kapton
Al

## Slide 22
Final Device
Fabrication
Glass
Au
Au
FTO
Kapton
Al

## Slide 23
Final Device
Fabrication
Glass
Au
Au
FTO
Kapton
Al
+ + + + + + + + + + + +
- - - - - - - - - - - -
+ + + + + + + + + + +

## Slide 24
Characterization

## Slide 25
Triboelectric Nanogenerator
Characterization

## Slide 26
Photodetector
Characterization
EQE
External quantum efficiency reflects the energy conversion efficiency from light to electric
Responsivity
Represents the photocurrent per unit of incident power
= photocurrent
Incident light power
Specific detectivity
Represents the ability of a device for capturing weak signal
= electron charge
Dark current
Effective area

## Slide 27
Photodetector
Characterization

## Slide 28
Photodetector
Characterization

## Slide 29
Conclusion

## Slide 30
Conclusion
EQE
Detectivity
Responsivity

## Slide 31
Thanks for your attention
Maedeh.taherkhani@sharif.edu
Maedehtaherkhani@gmail.com
Maedeh-taherkhani